## Slide 1: Data Mining In Wireless Networks
John Widhalm

## Slide 2: Introduction
What are Self Organizing Maps (SOMs)
  Structure
  Algorithm
  Demonstrations
Data Mining in Wireless Systems
  Metrics
  How SOMs can be used in ascertaining system behavior.
  Demonstrate using R

## Slide 3: Self-Organizing Maps (SOMs)
SOMs are a clustering and data visualization technique and are sometimes referred to as Kohonen maps after their inventor, Teuvo Kohonen[7].
The SOM is a technique which provides a way of reducing multidimensional space into one, two and sometimes three dimensions.
One of the most important features of the SOM in data mining is the visualization property.
  In a nutshell - SOMs show the similarity between objects.

## Slide 4: SOM Structure
A, example of a 4x4 lattice of nodes connected to the input layer (purple nodes) representing a two dimensional vector.
Each node has a specific topological position (x,y coordinate)
Each node contains a vector of weights (aka codebook vector) of the same dimension as the input vector.
  If training data consist of V vectors of n dimensions then . . .
  Each node will contain a corresponding weight vector W of n dimensions.
Figure 1 [2]
Each cell represents a node in the lattice

## Slide 5: SOM Structure (continued)
Figure 2
Each cell represents a node in the lattice
Example of a 40 x 40 lattice where each node in the lattice has three weights, one for each element of the input vector: red, green and blue.
Each node is represented by a rectangular cell.

## Slide 6: The SOM Algorithm
Initialize the weight of each node
  Set weights to a small random value
Choose an input vector at random. This vector will be presented to the SOM.
Find the Best matching Unit (BMU) by calculating the distance between the input vector and the weights of each node.
The radius of the neighborhood around the BMU is calculated. The size of the neighborhood decreases with each iteration.
Each node in the BMU’s neighborhood has its weight vectors adjusted to become more like the BMU. Nodes closest to the BMU are altered more than the nodes furthest away in the neighborhood.
Repeat from step-2; do until convergence

## Slide 7: Step-1: Initialize Weight of Each Node
The weight of each node is initialize to a value that is between 0 and 1 (0 < weight < 1).
These weights are also referred to as “codebook vectors.”

## Slide 8: Step-2: Choose a Random Vector

## Slide 9: Step-3: Calculate the Best Matching Unit
Calculating the BMU is done according to the Euclidean distance among the node’s weights (W1, W2, … , Wn) and the input vector’s values (V1, V2, … , Vn).
Euclidean distance is a measurement of similarity between two sets of data.

## Slide 10: Step-4: Determine the BMU Neighborhood
The size of the neighborhood is an exponential decay function that shrinks on each iteration until eventually the neighborhood is just the BMU itself.
Figure 3 [2]
The Initial BMU Neighborhood
The Exponential Decay Function
Where:

## Slide 11: Exponential decay
Figure 4 [2]
The ever shrinking radius
The exponential decay function reduces the radius at each iteration

## Slide 12: Step 5a – Modifying the Nodes Weights
The new weight for a node is the old weight, plus a fraction (L) of the difference between the old weight and the input vector, adjusted (theta) based on distance from the BMU.
The learning rate L is also an exponential decay function. This ensures that the SOM will converge.
Weight Update Function
The Exponential Decay Function
Notes: Lt – is the learning rate at time t
L0 – is the learning rate at time t0
t – is the iteration loop t
Lamda –s the time constant

## Slide 13: Step 5b – Modifying the Nodes Weights
The neighborhood is defined by a Gaussian curve so that nodes that are closer are influenced more than farther nodes.
Figure 5
Modifying the weights
Where:
Notes: The nodes that fall within the radius (shaded area) are updated

## Slide 14: SOM Demo
2-D square grid of nodes.
Inputs are colors – can you tell how many?
SOM converges so that similar colors are grouped together.
After x training cycles the values of the weight vectors (codebook vectors) will represent the distribution of the input vectors[7].
Notes: There are eight colors
red, green, blue, yellow, orange, purple, dk_green, dk_blue;

## Slide 15: See It In Action
Explain Algorithm Using Excel
SOM Demo
  Colors demo
  Using R

## Slide 16: CDMA Wireless Networks
Code Division Multiple Access (CDMA) is a cellular telephone technology which is covered by the 3GPP2 set of standards (CDMA2000).
CDMA, along with GSM/UMTS, WiMax, LTE are all cellular technologies.
CDMA is predominate in North America while GSM is predominate in Europe, Middle-East, and Asia.
A service provider, such as Sprint, Verizon, AT&T, Metro-PCS, builds their network based on one of these technologies.
Equipment providers, such as Alcatel/Lucent, Motorola, Ericsson, Huawei, build and sell the cellular equipment to the service providers.

## Slide 17: Wireless Network Reference Diagram
EV-DO RNC
A
B
PDSN
Backhaul Core Routers
PDSN Router
BTS – Cell Site
BTS – Cell Site
BTS – Cell Site
Internet
Access Side
Backhaul Transport Network
Core Network

## Slide 18: Reference Diagram - Terms
BTS – Basestation Transceiver Subsystem. This provides the air interface to the mobile. BTSs (aka cell sites) are peppered throughout a geographical area.
The backhaul transport carries traffic to/from the core network.
The core network is the final aggregation point for all BTSs. The Radio Node Controller (RNC) and Packet Data Serving Node (PDSN), along with a few other pieces of key equipment, reside here.
The RNC –Provides the network anchor point for all subscriber terminals from the BTS.
The PDSN – established PPP sessions for users and provides the gateway to the internet.

## Slide 19: CDMA EVolution Data Optimized (EV-DO)
EVDO was developed as an evolution to the CDMA2000 standard to support high data rates. 1xRTT is the voice portion of the standard.
The focus of this presentation will be on EV-DO

## Slide 20: Performance Metrics
A given system continuously captures and records hundreds of metrics about itself.
These metrics can be significantly reduced to a subset of key metrics. Engineers troll through these metrics identifying the key metrics that can best be used to describe the system behavior.
These metrics fall into two categories:
  Key Capacity Indicators (KCIs) are measurements like CPU Utilization and Link Utilization
  Key Performance Indicators (KPIs) are measurements like call completion rate, call failure rate.

## Slide 21: Metric Registers
Metrics are captures via registers. Registers can vary in size but are usually 32 or 64 bits in size.
Cumulative
  Register continuously increments with each sample interval
Non Cumulative
  Register captures delta between current measurement and previous measurement

## Slide 22: Register Examples
 | Cumulative | Non-Cumulative
13:00:00 | 10 | 
13:30:00 | 16 | 6
14:00:00 | 19 | 3
14:30:00 | 25 | 6
15:00:00 | 39 | 14
15:30:00 | 42 | 3
16:00:00 | 49 | 7
16:30:00 | 56 | 7
17:00:00 | 63 | 7
17:30:00 | 64 | 1
18:00:00 | 65 | 1
18:30:00 | 78 | 13
19:00:00 | 79 | 1
19:30:00 | 82 | 3
20:00:00 | 83 | 1
 | Cumulative | Non-Cumulative
13:00:00 | 10 | 
13:30:00 | 16 | 6
14:00:00 | 19 | 3
14:30:00 | 25 | 6
15:00:00 | 39 | 14
15:30:00 | 0 | -39
16:00:00 | 6 | 6
16:30:00 | 7 | 1
17:00:00 | 12 | 5
17:30:00 | 14 | 2
18:00:00 | 0 | -14
18:30:00 | 9 | 9
19:00:00 | 15 | 6
19:30:00 | 17 | 2
20:00:00 | 18 | 1
Problem – register is cycling

## Slide 23: Metric Formulas
Individual metrics themselves are rarely used because an individual metric rarely captures the specific behavior that an analyst is interested in.
Example: Session setup failure rate is made up of two individual metrics: Success Rate – Handoff Abort Rate.
  Key metrics can get much more complicated than this.
Key point is that key metric formulas are made up of several individual metrics.

## Slide 24: Post-Processing
Post processing of raw data can be complicated.
The table above lists metrics for four physical interfaces.
Post processing must be done carefully to avoid mixing metrics of one interface with another.
The is just one simple example. They can get much more complicated than this.

## Slide 25: Key Metrics
For the purpose of this tutorial we will be looking a few key metrics from the BTS.
  Failed Connection Attempts: A mobile attempted to connect to the system but failed to do so. Reasons could be RF congestion, backhaul congestion (refer to reference diagram), or other resource depletion such as licenses or channel elements.
  Dropped Connection Rate: Sessions usually drop when a user moves into a poor coverage area (poor RF conditions).

## Slide 26: Key Metrics (continued)
Metrics continued . . .
  Session Setup Failure Rate: Occurs when handoff fails between two systems.
  Session Setup Success Rate – just the inverse the failure rate previously described.
  TA Failure Rate: Terminal Access (mobile) Failure rate. A mobile terminal attempted to authenticate to the system but failed to do so. This occurs before the connection is attempted. Cause could be an invalid mobile (no longer in service) or even a malicious subscriber attempting to gain access to the system.

## Slide 27: Key Metrics (continued)
Metrics continued . . .
  Requested Data Rate From Cell: Data rate a given mobile has requested.
  Per User Throughput – data rate throughput to the mobile.

## Slide 28: CDMA Raw Data Summary
39 Cell Sites
Over a 30 week period
Sampled during the busy-hour
Total of 3,510 samples

## Slide 29: SOM Visualization
Codebook-vector Map
Arranged in a hexagonal fashion
The units are numbers from left to right, starting from the bottom left.
The first unit, for example, is characterized by relatively large values of Red and Green.
Neighboring units are more similar that those units which are further away.
A gradual transition occurs between codebook values.

## Slide 30: SOM Topology
SOM Topology can be chosen to be either hexagonal or rectangular.
Using the hexagonal topology each node can have up to six equivalent neighbors.
Using the rectangular topology each node can have four or eight neighbors – depending on implementation.

## Slide 31: Map Size
The map size in one of the most important parameters.
Larger maps allow for more detail and take more time to be created.
A 10x10 map of the same date illustrated as 5x5 on the previous chart.
Notice that with the added granularity more details of the structure of the data begins to emerge.

## Slide 32: SOM Map Size Comparison
Same data at different map sizes
To reiterate - the values of the weight vectors (codebook vectors) will represent the distribution of the input vectors[7].

## Slide 33: SOM Visualization Techniques
Different techniques are used to visualize the codebook vectors (weight vectors).
Two principal techniques we will investigate are:
  Component Planes: Show the relative values of one of the components of the codebook vectors[7].
    The number of component planes Is equal to the size of the input dimension.
  U-Matrices: Used to visualize the distances between the codebook vectors and is able to detect clusters and boundaries between them.

## Slide 34: See It In Action
SOM Demo Using R with BTS data

## Slide 35: Conclusion
Self Organizing Maps (SOMs) offer a unique approach to understand the underlying structure of the data.
It is very flexible and can cross a variety of disciplines
As algorithms go is relatively easy to use and understand.

## Slide 36
The End

## Slide 37: References
[1] Pang-Ning Tan, Michael Steinbach (2006), Vipin Kumar, “Introduction to Data Mining”, .Pearson Education.
[2] www.ai-junkie.com, Kohonen’s Self Organizing Feature Maps, February 2012.
[3] Kishan Mehrotra, Chilukuri K. Mohan, Sanjay Ranka (1997),Elements of Artificial Neural Networks, MIT Press.
[4] Laurene V. Fausett (1994), Fundamentals of Neural Networks, Prentice-Hall.
[5] http://chem-eng.utoronto.ca/~datamining/, Dr. Saed Sayad, Self Organizing Maps, University of Toronto, February 2012.
[6] Pekko Vehviliainen, Kimmi Hatonen, Pekka Kumpulainen, “Data Mining in Quality Analyst of Digital Mobile Telecommunications Network”, IMEKO World Congress, June 22 – 27, 2003, Dubrovnik, Croatia.
[7] Teuvo Kohonen, “Self-Organizing Maps”, Springer, Berlin, 2001
[8] Ron Wehrens, “Chemometrics with R”, Springer Publishing, 2011